## Slide 1
Dynamic Time Warping For Gait Analysis
TEAM 11
SUPVISED BY :
DR. EMAN
SBEG 207

## Slide 2
  Introduction
  Problem Definition
  Why DP
  How the Algorithm Works
  Results
  Challenges
  Conclusion
Summary

## Slide 3
Introduction

## Slide 4
  Gait analysis is a key tool in physical therapy and rehabilitation
  Used to assess recovery after stroke, injury, or neurological disorders
  Modern systems rely on sensor-based time-series data (accelerometers, IMUs, motion capture, cameras)
  A major challenge is comparing patient gait to a healthy reference
HOWEVER, COMPARING GAIT SIGNALS IS NOT STRAIGHTFORWARD, ESPECIALLY WHEN PATIENTS WALK AT DIFFERENT SPEEDS OR THE SIGNAL HAS NOISE.
Gait Analysis in Rehabilitation

## Slide 5
PROBLEM
Problem Definition
healthy signal but merely walking slower/noise
healthy signal
  Stroke patients often walk slower and irregularly
  Clinicians want to compare patient gait to a healthy reference
  Direct comparison fails due to speed differences

## Slide 6
Why Simple Distance Fails
  Euclidean distance assumes point-to-point alignment
  Speed differences → high error even if shapes match

## Slide 7
Why DP?

## Slide 8
Optimization
Efficiency
Reusability
Simplification
Scalability
Why DP is appropriate
OUR METHODOLOGY
  We need the optimal non-linear alignment
  Choices depend on previous alignments
  Overlapping subproblems → DP is ideal

## Slide 9
How does the Algorithm works?

## Slide 10
  Dynamic Time Warping compares two time-series by allowing non-linear alignment
  Instead of matching point A in healthy to point A in patient, DTW allows flexible matching:
    Repeats points
    Skips points
    Stretches or compresses time
  The goal is to find the minimum-cost alignment path between two sequences
Dynamic Time Warping
ALGORITHM INTUITION

## Slide 11
INPUT
  Inputs:
    Healthy Signal = [h₁, h₂, ..., hₙ]
    Patient Signal = [p₁, p₂, ..., pₘ]
  Output:
    Minimum alignment cost (similarity score)
    Optimal warping path
  Distance Metric:
OUTPUT
DISTANCE METRIC
Input and Output Definition

## Slide 12
  Subproblem
    = minimum cost to align
    first healthy points with first patient points
DP Formulation
  Base Cases
    First row/column = ∞ (or large number)
  Recurrence Relation:

## Slide 13
DP Table Construction & Backtracking
Values in brackets are part of the optimal backtracking path
CASE1: HEALTHY MACTH

## Slide 14
Complexity
  Time Complexity:
  Space Complexity:
CAN BE REDUCED TO O(MIN(N, M)) IF ONLY COST IS NEEDED

## Slide 15
Results

## Slide 16
Experimental Results
CASE1: HEALTHY MACTH

## Slide 17
Experimental Results
CASE2: SLOW PATIENT

## Slide 18
Experimental Results
CASE3: SEVERE ASYMETERY

## Slide 19
Live Demo

## Slide 20
Challenges

## Slide 21
  High Sensitivity to Noise (The "Outlier" Trap)
    Accelerometers are incredibly noisy. A simple bump of the sensor or a loose strap creates a "spike" in the data.
  The "Endpoint" Constraint
    Standard DTW assumes the sequences start and end at the same phase (e.g., both start at a heel strike).
3. Computational Complexity
    While fine for one stride, if you want to analyze a 10-minute walk at 100Hz, you have 60,000 points. A 60k x 60k matrix will crash a standard computer's memory.

## Slide 22
Conclusion
  We presented a Dynamic Programming–based system for gait analysis in rehabilitation.
  Dynamic Time Warping enables accurate comparison of gait patterns despite walking speed variations.
  The DP formulation guarantees an optimal non-linear alignment between patient and healthy signals.
  Experimental results show that DTW produces low similarity scores for biomechanically similar gaits, even when temporal distortions exist.
  This approach demonstrates how algorithmic techniques can solve real-world biomedical signal analysis problems.

## Slide 23
References
[1] F. Massaad, T. M. Lejeune, and C. Detrembleur, “The up and down bobbing of human walking: A compromise between muscle work and efficiency,” Journal of Physiology, vol. 582, no. 2, pp. 789–799, Jul. 2020, doi: 10.1113/jphysiol.2020.127969.
[2] H. S. Lee, “Application of dynamic time warping algorithm for pattern similarity of gait,” Journal of Exercise Rehabilitation, vol. 15, no. 4, pp. 526–530, 2019, doi: 10.12965/jer.1938384.192.
[3] W. Pirker and R. Katzenschlager, “Gait disorders in adults and the elderly: A clinical guide,” Wiener Klinische Wochenschrift, vol. 129, no. 3–4. Springer-Verlag Wien, pp. 81–95, Feb. 01, 2017. doi: 10.1007/s00508-016-1096-4.

## Slide 24
Thanks for your attention!